# Expanding the ports of a Raspberry PI using a MCP23S17.

The MCP23S17 is a 16-Bit I/O Expander with Serial (SPI) Interface . The topology of the design is shown below.

To control the ports of the part various registers need to be addressed. The full Raspberry code for doing this is included in this document. The register address map is shown below.

The basic registers are listed below:-

IODIR - I/O DIRECTION REGISTER

This controls the direction of the data I/O. When a bit is set, the corresponding pin becomes an input. When a bit is clear, the corresponding pin becomes an output.

For example to set all bits of portA to be outputs:-

  writeByte (IODIRA, 0x00) ;

and to set all bits of portB to be inputs:-

  writeByte (IODIRB, 0xFF) ;

Writing and reading data then becomes a simple matter of addressing the GPIO ports:-

  writeByte (GPIOA, <word>) ;
ie
  writeByte (GPIOA, 0xFF) ;

and reading the value of a port

  data = readByte (GPIOB) ;

IPOL - INPUT POLARITY REGISTER

This register allows the user to configure the polarity on the corresponding GPIO port bits.
If a bit is set, the corresponding GPIO register bit will reflect the inverted value on the pin.
For example to invert bit 1 of port A

  writeByte (IPOLB, 0x01) ;

GPPU - PULL-UP RESISTOR CONFIGURATION REGISTER

The GPPU register controls the pull-up resistors for the port pins. If a bit is set and the corresponding pin is configured as an input, the corresponding port pin is internally pulled up with a 100 kΩ resistor.

For more advanced features and to use interrupts see the MCP23S17 datasheet.

References:-
The following is included for further reading.

https://projects.drogon.net/piface-mk2/

http://www.open.com.au/mikem/bcm2835/

http://www.cmdrkeen.net/tag/spi/

http://www.linuxjournal.com/article/6908

Using the information in the above links the following code was put together to test out the basic features of the MCP23S17 part. The code is intended as a starting point only. Credit and recognition for figuring out how to drive this part goes to the authors of the above links.

To compile save to a file and compile with

  > gcc <filename>.c -o <filename>

/****************************************
* basic SPI demo for mcp23s17 *
*****************************************/
#include <stdlib.h>
#include <stdio.h>
#include <string.h>
#include <fcntl.h>
#include <sys/ioctl.h>
#include <linux/spi/spidev.h>
#include <sys/mman.h>
#include <sys/types.h>
#include <sys/stat.h>
#include <unistd.h>

#include <stdint.h>

#define CMD_WRITE	0x40
#define CMD_READ	0x41

static char *spiDevice = "/dev/spidev0.0" ;
static uint8_t spiMode = 0 ;
static uint8_t spiBPW = 8 ;
static uint32_t spiSpeed = 5000000 ;
static uint16_t spiDelay = 0;

// MCP23S17 Registers

#define	IOCON	0x0A

#define	IODIRA	0x00
#define	IPOLA	0x02
#define	GPINTENA	0x04
#define	DEFVALA	0x06
#define	INTCONA	0x08
#define	GPPUA	0x0C
#define	INTFA	0x0E
#define	INTCAPA	0x10
#define	GPIOA	0x12
#define	OLATA	0x14

#define	IODIRB	0x01
#define	IPOLB	0x03
#define	GPINTENB	0x05
#define	DEFVALB	0x07
#define	INTCONB	0x09
#define	GPPUB	0x0D
#define	INTFB	0x0F
#define	INTCAPB	0x11
#define	GPIOB	0x13
#define	OLATB	0x15

int spi_fd;

static uint8_t readByte (uint8_t reg)
{
  uint8_t tx [4] ;
  uint8_t rx [4] ;
  struct spi_ioc_transfer spi ;

  tx [0] = CMD_READ ;
  tx [1] = reg ;
  tx [2] = 0 ;

  spi.tx_buf = (unsigned long)tx ;
  spi.rx_buf = (unsigned long)rx ;
  spi.len = 3 ;
  spi.delay_usecs = spiDelay ;
  spi.speed_hz = spiSpeed ;
  spi.bits_per_word = spiBPW ;

  ioctl (spi_fd, SPI_IOC_MESSAGE(1), &spi) ;

  return rx [2] ;
}

static void writeByte (uint8_t reg, uint8_t data)
{
  uint8_t spiBufTx [3] ;
  uint8_t spiBufRx [3] ;
  struct spi_ioc_transfer spi ;

  spiBufTx [0] = CMD_WRITE ;
  spiBufTx [1] = reg ;
  spiBufTx [2] = data ;

  spi.tx_buf = (unsigned long)spiBufTx ;
  spi.rx_buf = (unsigned long)spiBufRx ;
  spi.len = 3 ;
  spi.delay_usecs = spiDelay ;
  spi.speed_hz = spiSpeed ;
  spi.bits_per_word = spiBPW ;

  ioctl (spi_fd, SPI_IOC_MESSAGE(1), &spi) ;
}

/*spi_open
* - Open the given SPI channel and configures it.
* - there are normally two SPI devices on your PI:
* /dev/spidev0.0: activates the CS0 pin during transfer
* /dev/spidev0.1: activates the CS1 pin during transfer
*
*/
int spi_open(char* dev)
{
  if((spi_fd = open(dev, O_RDWR)) < 0){
    printf("error opening %s\n",dev);
    return -1;
  }
  return 0;
}

int main(int argc, char* argv[])
{
    unsigned char data = 0xAF;
    if(argc <= 1){
        printf("too few args, try %s /dev/spidev0.0\n",argv[0]);
        return -1;
    }
    // open and configure SPI channel. (/dev/spidev0.0 for example)
    if(spi_open(argv[1]) < 0){
        printf("spi_open failed\n");
        return -1;
    }

  writeByte (IODIRA, 0x00) ;	// Port A -> Outputs
  writeByte (GPIOA, 0xFF) ;
  //writeByte (IPOLB, 0x01) ; // invert lsb
  //writeByte (GPPUB, 0xFF) ; // enable pullups.
  writeByte (IODIRB, 0xFF) ;	// Port B -> Inputs
  data = readByte (GPIOB) ;

  printf("RECEIVED: %.2X\n",data);
  close(spi_fd);
  return 0;
}